        PROGRAMMING WITH PYTHON

CLASS PROJECT—7

PROGRAM—1

#photo shoot
import os

def takesnap():
os.system("fswebcam -F 4 --fps 20-r 800*600 /home/cl213/HarshithaGowda/temp.jpg")
print("image take")
return
takesnap()

OUTPUT

PROGRAM—2

#Libraries
import RPi.GPIO as GPIO
import time

#GPIO Mode (BOARD / BCM)
GPIO.setmode(GPIO.BCM)

#set GPIO Pins
GPIO_TRIGGER = 18
GPIO_ECHO = 24

#set GPIO direction (IN / OUT) HARSHITHA
GPIO.setup(GPIO_TRIGGER, GPIO.OUT)
GPIO.setup(GPIO_ECHO, GPIO.IN)

def distance():
    # set Trigger to HIGH
    GPIO.output(GPIO_TRIGGER, True)

    # set Trigger after 0.01ms to LOW
    time.sleep(0.00001)
    GPIO.output(GPIO_TRIGGER, False)

    StartTime = time.time()
    StopTime = time.time()

    # save StartTime

    while GPIO.input(GPIO_ECHO) == 0:
        StartTime = time.time()

    # save time of arrival
    while GPIO.input(GPIO_ECHO) == 1:
        StopTime = time.time()

    # time difference between start and arrival
    TimeElapsed = StopTime - StartTime
    # multiply with the sonic speed (34300 cm/s)
    # and divide by 2, because there and back
    distance = (TimeElapsed * 34300) / 2

    return distance

if __name__ == '__main__':
    try:
        while True:
        dist = distance()
        print ("Measured Distance = %.1f cm" % dist)
        time.sleep(1)
        if (dist>100):
        print("distance is above 100")
        break

        # Reset by pressing CTRL + C
    except KeyboardInterrupt:
        print("Measurement of distance has been stopped by User")
        GPIO.cleanup() HARSHITHA

OUTPUT:

Measured distance = 4.8 cm
Measured distance = 5.4 cm
Measured distance = 5.8 cm
Measured distance = 4.0 cm
Measured distance = 5.6 cm
Measured distance = 6.3 cm
Measured distance = 9.5 cm
Measured distance = 5.2 cm
Measured distance = 3485 cm
distance is above 100.

        HARSHITHA
        CL-2
        ECE=C-SECTION